## Slide 1
Method of Moments based on a surface admittance operator (MoM-SO):
An Introduction
Adilton Junio Ladeira PEREIRA
adt@ufmg.br
Programa de Pós-Graduação em Engenharia Elétrica (PPGEE)¹
Belo Horizonte, julho de 2024
¹ Universidade Federal de Minas Gerais – Av. Antônio Carlos 6627. Belo Horizonte, MG, Brasil. 31270-901.

## Slide 2
Agenda
Introduction
    Motivation
    Differential Surface Admittance Concept
Circular Conductors Surrounded by a Homogeneous Lossless Medium
    Problem Statement
    Surface Admittance Operator
    Electric Field Integral Equation (EFIE)
    Discrete Green’s Function
p.u.l. Impedance
    Partial p.u.l. Impedance
    Total p.u.l. Impedance
Examples
    Bifilar Line
    Coaxial (single core) Cable

## Slide 3
MoM-SO is a numerical technique for calculating the series impedance matrix, , of systems with round conductors (wires and cables) which takes into account both skin and proximity effects.
Analytical formulation accounts only for the skin effect, assuming a symmetrical distribution of current in all conductors. However, the proximity effect can significantly affect transient voltages and should therefore be considered [1].
The surface-based approach operator (SO) requires only the discretization of the surface of the conductors, in contrast with volume-based approaches that mesh the entire cable cross-section, such as finite elements and conductor partitioning [2].
Motivation
Introduction

## Slide 4
Differential Surface Admittance Concept
On the boundary , consider the tangencial component of the magnetic field, [3]
Inside , the longitudinal componente of the electric field satisfies the Helmholtz equation:
with
Original Problem
Introduction

## Slide 5
Applying the Equivalence Principle [4], suppose that the constitutive parameters of the conducting cylinder are replaced by those of the medium outside the conductor.
Differential Surface Admittance Concept
with
The corresponding fictitious electric field in , , now satisfies
Equivalent Problem
Introduction

## Slide 6
To ensure a unique field solution, it suffices to introduce an equivalent surface current density, , related to the tangencial components of the field on the boundary, .
Differential Surface Admittance Concept
Equivalent Problem
By means of the differential surface admittance operator, :
The Dirichlet–Neumann operators, and , establish the boundary conditions on in relation to the values of the normal derivatives of the fields [3].
Introduction

## Slide 7
Multiconductor transmission (MTL) line with parallel solid cylindrical conductors and parallel hollow cylindrical conductors.
Problem Statement
Simplifying assumptions of the 2D quasi-TM approach:
the conductors are invariable along the direction (uniform transmission line),
the cross-section of each conductor is much smaller than the wavelength at the frequencies of interest.
Circular Conductors Surrounded by a Homogeneous Lossless Medium
The impedance matrix, , of parallel conductors satisfies the Telegrapher’s equation [5]:
, per unit length (p.u.l.) resistance matrix;
, per unit length (p.u.l.) inductance matrix;
, potencial vector;
, current vector;

## Slide 8
Surface Admittance Operator of the MTL
In the MoM-SO, the conductors are replaced by the surrounding medium and equivalent currents, , on each conductor’s boundary, [6].
governs the accuracy of the field representation inside the conductor. By setting , the electric field is assumed to be circularly-symmetric [6].
Fourier coefficients are one of the unknown variables in the MoM-SO formulation.
Circular Conductors Surrounded by a Homogeneous Lossless Medium
The longitudinal electric field on the boundary of the conductors, , can be expand by a truncated Fourier series [7]:

## Slide 9
Surface Admittance Operator of the MTL
If th-conductor is solid,
otherwise, if th-conductor is hollow then,
Circular Conductors Surrounded by a Homogeneous Lossless Medium
The electric field coefficients from all surface conductors can be assemble into a global vector of unknowns, .
The size of is , where

## Slide 10
Surface Admittance Operator of the MTL
The scaling factor has been introduced to make the coefficient equal to the current flowing in the -th conductor [7].
In a similar manner, we collect all the Fourier coefficients of the equivalent currents into a global vector
Circular Conductors Surrounded by a Homogeneous Lossless Medium
The equivalent surface current on the boundary of the conductors, , can be expand by a truncated Fourier series:

## Slide 11
Surface Admittance Operator of the MTL
At this point, we can relate vectors and by a global surface admittance operator, , as
where is a block diagonal matrix; is the sub-matrix of the surface admittance operator of the solid conductor; and , , e are those of the hollow conductor.
solid conductors
hollow conductors
are the conductors number; and are the surfaces number.
Recalling that,
Circular Conductors Surrounded by a Homogeneous Lossless Medium

## Slide 12
Surface Admittance Operator of the MTL
,
, , , e are diagonal matrices with entries:
is the Bessel function of the -th order of the first kind;
and denote Hankel functions of the -th order, respectively, first and second kind;
and are the derivatives of the Hankel functions and , respectively.
for
Circular Conductors Surrounded by a Homogeneous Lossless Medium

## Slide 13
Surface Admittance Operator of the MTL
In essence, the surface admittance concept is a simpler representation of the conductor which will allow us to simplify our original problem, just like Norton theorem helps simplify a circuit.
Using the surface admittance relationship, one can replace the conductor by an equivalent current source. Analogously, the surface admittance operator is the ratio of equivalent current and the electric fields on the boundary of the conductor.
Circular Conductors Surrounded by a Homogeneous Lossless Medium
Express as a truncated Fourier series
Apply the Equivalence Principle and introduce an equivalent surface current density,
Multiconductor
Transmission Line
subject to a Dirichlet boundary condition
Apply the boundary conditions to the tangential field components (Uniqueness Theorem)
Express as a truncated Fourier series

## Slide 14
Electric Field Integral Equation (EFIE)
Circular Conductors Surrounded by a Homogeneous Lossless Medium
Using the superposition principle, vector potential can be expanded as
is the contribution due to the equivalent currents on the -th surface conductor, .
The -th surface conductor, , can be traced by the position vector in a cylindrical coordinate system:
The effect of the equivalent current sources onto surrounding medium is modelled with the Electric Field Integral Equation (EFIE):
is the electric field -component at position ;
is the magnetic vector potential -component at position .
is the scalar potential.

## Slide 15
Electric Field Integral Equation (EFIE)
If conductor is solid, then
Circular Conductors Surrounded by a Homogeneous Lossless Medium
while, if conductor is hollow
The quasi-static Green’s function is only accurate when [7]:
the cross-section of the cable is much smaller than a wave-length, so that the retardation effect may be neglected (the smallest wavelength of interest is 30 m at 10 MHz); and
the surrounding medium is lossless.
Consider the frequency independent (quasi-static) Green’s function of a two-dimensional homogeneous space:

## Slide 16
Electric Field Integral Equation (EFIE)
Circular Conductors Surrounded by a Homogeneous Lossless Medium
On the boundary of the -th conductor, reads:
and represent the entry of the p.u.l. resistance and inductance matrices, respectively; and
Note that , , , and on concern the surface of the solid conductor; those on concern the outer surface of the hollow conductor, and those on concern the inner surface of the hollow conductor.
The main goal is to solve the p.u.l. impedance parameters, which will be done numerically by the MoM using the Fourier series expansions.
Relating the potential drop to the p.u.l. impedance parameters through the Telegrapher’s equation:

## Slide 17
Discrete Green’s Function
Circular Conductors Surrounded by a Homogeneous Lossless Medium
Given an multiconductor cylindrical geometry, one can approximate the field and the current on the -th surface conductor by means of a truncated Fourier series:

## Slide 18
Circular Conductors Surrounded by a Homogeneous Lossless Medium
Applying the Galerkin method and using the orthogonality relationship to both sides of :
Matrix
Discrete Green’s Function

## Slide 19
Circular Conductors Surrounded by a Homogeneous Lossless Medium
Matrix describes the contribution of the equivalent current on -th conductor to the field on the boundary of the -th conductor. denotes the entry of the matrix , given by the double integral:
which may be evaluated analytically [7]. Then, the field on the -th surface conductor can be compactly written as:
Using the matrix notation, can be rewrite as
Discrete Green’s Function

## Slide 20
Circular Conductors Surrounded by a Homogeneous Lossless Medium
Equation is the discretized EFIE that allows to capture the proximity between the conductors;
Indeed, the non-diagonal blocks in capture the mutual impedance between the conductors [7].
Consider an matrix. In the -th column:
if the -th conductor is solid (), the row corresponding to the position of is “1”;
If the pth conductor is hollow , the rows corresponding to the positions of and are “1”;
All other entries of are zeros.
Then, one can relate the equivalent currents, , with the conduction currents through:
Discrete Green’s Function
Global matrix is obtained by the discretization of Green’s function and given by

## Slide 21
Circular Conductors Surrounded by a Homogeneous Lossless Medium
Discrete Green’s Function
Unknown Quantities: , ,
MoM
Telegrapher’s equation
p.u.l. Impedance
EFIE
Express as a truncated Fourier series
Apply the Equivalence Principle and introduce an equivalent surface current density,
Multiconductor
Transmission Line
subject to a Dirichlet boundary condition
Apply the boundary conditions to the tangential field components (Uniqueness Theorem)
Express as a truncated Fourier series

## Slide 22
Partial p.u.l. Impedance
p.u.l. Impedance
The partial p.u.l. parameters can be computed by combining the surface admittance relation and the discretized EFIE.
First left multiply by , and use to obtain:
The equivalent current may be expressed as
Since all materials in the cable are linear, the p.u.l. impedance must be independent from the current flowing in the conductors.
Hence, the expression inside the square bracket on the right-hand side of must be equal to the identity matrix.
where 1 is the identity matrix. Next, we left multiply equation above by to get:
The partial p.u.l. impedance relates the scalar potential and current in each conductor of a MTL.
In order to know the total current in each conductor, it’s possible to perform reduction of the partial p.u.l. impedance on the total p.u.l. impedance parameters.

## Slide 23
Total p.u.l. Impedance
p.u.l. Impedance
For a configuration in which multiple conductors are lumped into the same line, is desirable to relate line potential, , with line current, .
relate with conductor current, , through:
On the -th row of , ‘1’s are present in the columns corresponding to the conductors which are part of the -th line, and all other columns are zero.
Incidence Matrix state that the is equal to the sum of currents in conductors of that particular line.
where is the partial p.u.l. impedance, computed by the MoM-SO theory.
Replacing and into ,
which enforces that the scalar potentials of all conductors in the same line are identical.
Telegrapher’s equation which relates conductor currents and conductor potentials is given by
Matrix can also relate line potentials, , and conductor potentials, , as
where is the impedance matrix of dimension equal to number of lines (active and reference).

## Slide 24
Total p.u.l. Impedance
p.u.l. Impedance
Procedure to Calculate the Total P.u.l. Impedance
1. Store line voltages of each active line with respect to the reference line in vector . Likewise, the line currents of all active lines are stored in vector . The Telegrapher’s equation
relates the line voltages and currents by the total p.u.l. impedance matrix, .
2. Relate voltages and line potentials , and currents and through a incidence matrix :
For practical applications, the total p.u.l. impedance relates voltages with currents of all active lines.
Fot this reduction procedure, set any conductor as reference for the voltages and as return path for the currents.
Line is a group of one or more conductors which are kept at the same potential and carry the same signal;
Return line is used as reference for the voltage of the corresponding line, and carries the return current.
Line voltages are defined as the difference between the potential of an active line and its corresponding return line.

## Slide 25
Total p.u.l. Impedance
p.u.l. Impedance
is made up of ‘1’s, ‘0’s, and ‘-1’s:
In the -th row, there is a “1” in the column corresponding to the active line’s line number; and
“-1” in the column corresponding to the line number of its return line.
3. Replacing and into Telegrapher’s equation ,
Multiplying both sides by
Using the fact that and , it’s possible to grouping terms in right-hand of into a single inverse:
4. Replacing both equations into ,

## Slide 26
Circular Conductors Surrounded by a Homogeneous Lossless Medium
Total p.u.l. Impedance
MoM
Telegrapher’s equation
p.u.l. Impedance
EFIE
Express as a truncated Fourier series
Apply the Equivalence Principle and introduce an equivalent surface current density,
Multiconductor
Transmission Line
subject to a Dirichlet boundary condition
Apply the boundary conditions to the tangential field components (Uniqueness Theorem)
Express as a truncated Fourier series
Total p.u.l. Impedance,

## Slide 27
Bifilar Line
Examples
1. Global dimension for
2. Fourier coefficients vectors:
and
3. Surface admittance operator

## Slide 28
Bifilar Line
Examples
4. Green’s Sub-Matrices
4.1 Self-conductors – Equations (52), (53) [1]:
4.2 Mutual-conductors:
4.2.1 Central Column (): Equations (45), (46) [1]:

## Slide 29
Bifilar Line
Examples
4.2.3 Negative Columns (): Equation (51) [1]:
* denotes complex conjugation.
4.2.2 Positive Columns (): Equations (49), (50) [1]:
With being the binomial coefficient.

## Slide 30
Bifilar Line
Examples
5. Full Green’s Matrix:
6. Incident Matrices:
Line #1 (Active)
Line #2 (Return)
Conductor
Conductor
Active Line #1
Line #2 (Return)
Line #1 (Active)
Conductor
Conductor

## Slide 31
Bifilar Line
Examples
MoM-SO ()
MoM-SO ()

## Slide 32
Bifilar Line
Examples
MoM-SO ()
MoM-SO ()
MoM-SO ()

## Slide 33
Single core (coaxial) cable
Examples
,
;
2. Green’s self-elements – Equations (52), (53) [1]:
1. Global dimension for
3. Green’s mutual-elements – Equations (B.8), (B.17) [7]:

## Slide 34
Single core (coaxial) cable
Examples
4. Green’s Matrix and Sub-Matrices – Appendix B [7]:
,
;

## Slide 35
Single core (coaxial) cable
Examples
,
;
5. Incident Matrices:

## Slide 36
Single core (coaxial) cable
Examples
;
()
()

## Slide 37
Single core (coaxial) cable
Examples
;

## Slide 38
Single core (coaxial) cable
Examples
()
()
;

## Slide 39
[1] U. R. Patel, B. Gustavsen and P. Triverio, "An Equivalent Surface Current Approach for the Computation of the Series Impedance of Power Cables with Inclusion of Skin and Proximity Effects," in IEEE Transactions on Power Delivery, vol. 28, no. 4, pp. 2474-2482, Oct. 2013, doi: 10.1109/TPWRD.2013.2267098.
[2] U. R. Patel, B. Gustavsen and P. Triverio, "Proximity-Aware Calculation of Cable Series Impedance for Systems of Solid and Hollow Conductors," in IEEE Transactions on Power Delivery, vol. 29, no. 5, pp. 2101-2109, Oct. 2014, doi: 10.1109/TPWRD.2014.2330994.
[3] D. De Zutter and L. Knockaert, "Skin effect modeling based on a differential surface admittance operator," in IEEE Transactions on Microwave Theory and Techniques, vol. 53, no. 8, pp. 2526-2538, Aug. 2005, doi: 10.1109/TMTT.2005.852766.
[4] R. F. Harrington, Time-harmonic electromagnetic fields. New York, NY: McGraw-Hill, c2001. xiii, 480 p.
[5] C. R. Paul, Analysis of Multiconductor Transmission Lines, 2nd ed. Hoboken, NJ, USA: Wiley, 2007.
[6] Tanaka, Y. et al. Development of a Computer Program for Calculating the Transmission-Line Constants of Cables Installed in a Tunnel Taking the Skin and Proximity Effects into Account. Proc. of International Conference on Power Systems Transients (IPST), Seoul, Republic of Korea. June 26-29, 2017
[7] U. R. Patel, A Surface Admittance Approach For Fast Calculation of the Series Impedance of Cables Including Skin, Proximity, and Ground Return Effects. 2014. University of Toronto, Graduate Department of The Edward S. Rogers Sr. Department of Electrical & Computer Engineering.
Reference